## Slide 1
김정인
jikim@imguru.co.kr
강의환경 : raspberry pi 확장 보드 , ubuntu 18.04
강의 자료 공유 서버 :
ftp-server : 156.147.178.101
id : linux
passwd : 없음
강의자료 배포 : 01_day 폴더
01_day.ppt
강의 시간 : 40분 - 15 ~ 20 휴식
11시 45분 - 13시 05분

## Slide 2
sysfs를 이용한 하드웨어 제어
# vi blink.sh
#!/bin/sh echo 16 > /sys/class/gpio/export echo out > /sys/class/gpio/gpio16/direction while true do echo 1 > /sys/class/gpio/gpio16/value
sleep 1 echo 0 > /sys/class/gpio/gpio16/value
sleep 1 done
# sh blink.sh

## Slide 3
wiringled.c
#include <wiringPi.h>
#include <stdio.h>
#include <stdlib.h>
int ledControl(int gpio)
{
int i;
pinMode(gpio, OUTPUT) ;
for (i = 0; i < 5; i++) {
digitalWrite(gpio, HIGH);
delay(1000);
digitalWrite(gpio, LOW);
delay(1000);
};
return 0;
}
int main(int argc, char** argv)
{
int gno;
if(argc < 2) {
printf("Usage : %s GPIO_NO\n", argv[0]);
return -1;
}
gno = atoi(argv[1]);
wiringPiSetup();
ledControl(gno);
return 0;
}

## Slide 4
wiringswitch.c
#include <wiringPi.h>
#include <stdio.h>
#define SW 4 /* GPIO23 */
#define LED 27 /* GPIO16 */
int switchControl()
{
pinMode(SW, INPUT);
pinMode(LED, OUTPUT);
while (1) {
if(digitalRead(SW) == LOW) {
digitalWrite(LED, HIGH);
delay(1000);
digitalWrite(LED, LOW);
delay(1000);
}
};
return 0 ;
}
int main(int argc, char** argv)
{
wiringPiSetup();
switchControl();
return 0 ;
}

## Slide 5
#define _IO(type,nr) _IOC(_IOC_NONE,(type),(nr),0)
#define LED_ON _IO( ’c’, 1 )
0
0
1
0
0
0
1
1
0
0
0
1
1
0
0
0
0
0
0
0
1
nr
‘c’
size
dir
’a’ => 97
’A’ => 65
’0’ => 48
’\n’ => 10
’\r’ => 13
’\t’ => 9
’ ’ => 32
99 => 01100011
type

## Slide 6
#define _IO(type,nr) _IOC(_IOC_NONE,(type),(nr),0)
#define LED_ON _IO( ’c’, 1 )
0
0
0
0
1
1
0
0
0
1
1
0
0
0
0
0
0
0
1
nr
‘c’
size
dir
’a’ => 97
’A’ => 65
’0’ => 48
’\n’ => 10
’\r’ => 13
’\t’ => 9
’ ’ => 32
99 => 01100011
type

## Slide 7
#include <sys/mman.h>
#include <fcntl.h>
#include <unistd.h>
#include <stdio.h>
#include <string.h>
#include <stdlib.h>
int main()
{
int fd;
char *p;
fd = open("aaa", O_RDWR );
ftruncate(fd, 100);
p = mmap( 0 , 100, PROT_READ | PROT_WRITE, MAP_SHARED, fd, 0);
strcpy(p, "hello");
munmap(p, 100);
close(fd);
return 0;
}
“hello”
“hello”

## Slide 8
_IOC_TYPECHECK(size)
(sizeof(t) == sizeof(t[1])
_IOC_TYPECHECK(4)
sizeof(4) == sizeof(4[1])
_IOC_TYPECHECK(int)
sizeof(int)
sizeof(int) == sizeof(int[1])

## Slide 9
#include <linux/mm.h>
int my_mmap (struct file *filp, struct vm_area_struct *vma)
{
unsigned long pfn;
printk("my_mmap()\n");
printk("vm_start=%p, vm_end=%p\n", (void*)vma->vm_start, (void*)vma->vm_end );
pfn = virt_to_phys((void*)page)>>12;
remap_pfn_range(vma, vma->vm_start, pfn, 4096, vma->vm_page_prot);
return 0;
}

## Slide 10
0x76f20000
0x76f21000
“hello”